DetectionSlicer
Conversion of Energy Depositions in LAr in PE Detections

---
Goal: convert Edep to NPE
1. Workflow:
2. Optical Map: convert Edep to PE detected based on the deposit coordinates.
3. Hit-Space Distribution: spread PE detected over the fibers shroud.

---
Output Format (1)
The output file contains:
  - fTree: flat Ttree with step-level information, see next slide
  - NInnerSlices: number of X-Y slices of the Inner Shroud
  - NOuterSlices: number of X-Y slices of the Outer Shroud
The output filename includes the parameters
e.g.: SlicedDetections9870294_Slices12_20_Yield40_QuantumEff0.400000_Seed123456789
  - SlicedDetections: prefix
  - 9870294: suffix of the original input file (e.g. output9870294.root)
  - Slices12_20: number of inner, outer slices
  - Yield40: number of OP per KeV
  - QuantumEff0.400000: quantum efficiency
  - Seed123456789: seed used to inizialize the TRandom generator

---
Output Format (2)
fTree format:
  - eventnumber: event identifier (from simulation file)
  - time: time in ns from the begin (from simulation file)
  - x, y, z: coordinates in mm (from simulation file)
  - material: name of the material (from simulation file)
  - energydeposition: energy deposited in KeV (from simulation file)
  - pedetected: number of photons detected by SiPM
  - detectionefficiency: detection efficiency (from Optical Map)
  - quantumefficiency: constant quantum efficiency
  - InnerSlice0, …, InnerSliceN: number of photons detected by
    each slice of the inner shroud
  - OuterSlice0, …, OuterSliceM: number of photons detected by
    each slice of the outer shroud